## Slide 1: QCar System Identification and CARLA Digital Twin Development
ZHANG Haolin, ZHANG Shiyu, WANG Qixin
Apr 22, 2024

## Slide 2: A brief word
The QCar dataset now are publicly available at
  https://github.com/QixinWangCpsLab/QCarDataSet
  (The corresponding paper, QCar Data Set for Building QCar Digital Twins, is under drafting)
Case Study: QCar Digital Twin

## Slide 3: Table of Contents
Background
QCar Dataset
QCar System Identification
QCar Digital Twin in Carla

## Slide 4: Background
Real-world traffic inferences exist in real-world smart vehicle datasets
  Sometimes, it is good, especially for exploring driving policy
  Sometimes, it is terrible because it constraints the state space
Conducting smart vehicle experiments in labs is impractical
  Huge space cost and finial cost

## Slide 5: Background
Conduct experiments in labs with
  Miniaturized Smart Vehicle (MinSV)
  Miniaturized Road System (MinRS)
Might also be impossible to build a large dataset when considering
  Wear down issue
  Huge time cost

## Slide 6: Background
Create a digital twin can solve this issue
  real-world MinSV (PHY-MinSV) -> cyber-world MinSV digital twin (DT-MinSV)
  real-world MinRS (PHY-MinRS) -> cyber-world MinRS digital twin (DT-MinRS)
Then, the data collection experiment could be conducted in a hybrid mode (aka “emulation”)
  Part of experiment are in the real world and the rest are in the cyber world
In addition, the DT-MinSV can be used for other tasks
  E.g., online decision making

## Slide 7: Background
To build DT-MinSV, large number of real-world driving data of PHY-MinSV are needed
  PHY-MinSV involves sophisticated nonlinear component
  Demands big data based (instead of analytical) system identification

## Slide 8: QCar Dataset
Quanser QCar is our PHY-MinSV
  Sensor Rich
  A similar dynamic behavior to an on-road vehicle
    4WD 1/10 RC Platform
  User friendly API
Quanser QCar Sensors
from Quanser, available at https://www.quanser.com/products/qcar/

## Slide 9: QCar Dataset
OptiTrack system records the QCar’s trajectory
  A vision-based positioning system
    Camera array (6 cameras in our setup)
    Rigid body Marker (placed on QCar)
  High Accuracy
    Sub-millimeter error
  High Refresh Rate
    Maximal 250 frame per second
OptiTrack System
from OptiTrack, available at https://www.quanser.com/products/qcar/

## Slide 10: QCar Dataset
Data Collection Campaign
  The 2022 Campaign
    PHY-MinRS: Track-and-Field Road System from the QCar package
    The QCar is derived by a human operator, aka the Manual Drive controller, through an Xbox Controller.
      Note: The control signal is the raw percentage of the throttle and steering. No additional control algorithm is applied.
    Experiment Settings
      Clockwise, Forward
      Clockwise, Backward
      Counterclockwise, Forward
      Counterclockwise, Backward

## Slide 11: QCar Dataset
Data Collection Campaign
  The 2023 Campaign
    PHY-MinRS: Straight Road System from the QCar package
    The QCar is steered by two controller
      Closed-loop controller: A line following program came with the QCar
      Open-loop controller: Always output steering signal of 0 to the QCar
    The throttle is from one of the five signal generators
      Sine wave
      Triangle wave
      Constant Function
      Square Root Function
      Quadratic Function

## Slide 12: QCar Dataset
Experiment Procedure
(re)Calibrate the OptiTrack System
Setup MinRS
Sensor Reading
OptiTrack System
Onboard Sensor
Controller
Cached Logs
Flush the logs to the disk
Run at 20Hz

## Slide 13: QCar Dataset
Available at https://github.com/QixinWangCpsLab/QCarDataSet
File Structure
\---QCarDataSet
+---linefollow_constant
| - 2023_0.csv
| - 2023_1.csv
| ……
+---manual_clockwise_backward
+---openloop_triangle
……
Root Directory
Line follow Steering Controller with the constant throttle Controller
The data segment with id=0, collected in the 2023 campaign
The QCar is driven by a Manual Drive controller backward and clockwise around the track.

## Slide 14: QCar Dataset
Data Format
  CSV format. Each data field is separated by a comma (,).
  Within each tick,
Column | Physical Meaning | Unit | Value
1 | Tick Time () |  | 
2-3 | Throttle & Steering Control () | (percentage) | 
4 | On-wheel Linear Speed () |  | 
5-7 | Gyroscope Reading ()* |  | 
8-10 | Accelerometer Reading ()* |  | 
11-13 | Position ()# |  | 
14-17 | Orientation ()# | in quaternion | 
18 | Battery Voltage () |  | 
Column | Physical Meaning | Unit | Value
1 |  |  | 
2-3 |  |  | 
4 |  |  | 
5-7 |  |  | 
8-10 |  |  | 
11-13 |  |  | 
14-17 |  | in quaternion | 
18 |  |  | 
* means in the vehicle frame of reference; # means in the global (inertial) frame of reference

## Slide 15: QCar Dataset
Data Format
  Sample data segment (available at https://github.com/QixinWangCpsLab/QCarDataSet/blob/main/sample.csv)
    (not all columns are listed here due to the length limit)

## Slide 16: QCar Dataset
Segmentation Issue
  The time of data collected in the 2022 campaign may not start from zero
    the human operator accidentally released the safety button during several trials
  Position or Orientation failed to update
    The QCar runs out of the view of OptiTrack System
    Package loss due to network
As people have different thoughts to tackle this issue, the released dataset is not being processed but the original output. The user shall process the data as needed.

## Slide 17: QCar System Identification
We try to identify the longitudinal model of the QCar
According to Rajesh, longitudinal dynamics is a joint behavior from the motor, tire, aerodynamic, rolling resistance, and gravitational forces
Theoretical Model:
Reference: Rajesh Rajamani, Vehicle Dynamics and Control Second Edition, 2012, Springer
Red: unknown coefficient or relationship

## Slide 18: Method 1: Linear SI

## Slide 19: Method 2: Naive PhyTaylor SI
PhyTaylor
Taylor Augmentation Order 1
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
One-hop Fully Connected Linear Layer (without Link Editing)
Activation Function:
Activation Function:
Activation Function:
Activation Function:
encoder reading (corresponding to wheel angle)
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Inspired by the physical knowledge
(Augmented)

## Slide 20: Link Editing:
PhyTaylor
Taylor Augmentation Order 1
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
One-hop Fully Connected Linear Layer (with Link Editing)
Activation Function:
Activation Function:
Signal Compressor
Signal Compressor
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
1
Edge 0  0, 1  0: 1.0;
Edge 2  0, 3  0: 0;
Edge others  0: *.
Method 3: Fine Tuned PhyTaylor for
weight = known constant
weight to be learnt
weight = 0

## Slide 21: Link Editing:
PhyTaylor
Taylor Augmentation Order 1
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
One-hop Fully Connected Linear Layer (with Link Editing)
Activation Function:
Activation Function:
Signal Compressor
Signal Compressor
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
1
Edge 0  0, 1  0: 1.0;
Edge 2  0, 3  0: 0;
Edge others  0: *.
Edge 0  1, 1  1: 0;
Edge 2  1, 3  1: 1.0;
Edge others  1: *.
Method 3: Fine Tuned PhyTaylor for

## Slide 22: Link Editing:
PhyTaylor
Taylor Augmentation Order 1
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Activation Function:
Activation Function:
Signal Compressor
Signal Compressor
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
1
Method 4: Fine Tuned PhyTaylor for
3 Layer-MLP
Similar to

## Slide 23: Link Editing:
PhyTaylor
Taylor Augmentation Order 1
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Signal Compressor
Activation Function:
Activation Function:
Signal Compressor
Signal Compressor
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
1
Method 4: Fine Tuned PhyTaylor for
3 Layer-MLP
Similar to

## Slide 24: Preliminary Result
Name | Loss of X | Loss of V
Linear | 1.73E-03 | 6.45E-01
Naïve | 3.94E-03 | 4.75E-01
 | 1.38E-03 | 4.52E-01
 | 2.5E-03 | 4.36E-02
Name | Loss of X | Loss of V
Linear | 1.73E-03 | 6.45E-01
Naïve | 3.94E-03 | 4.75E-01
 | 1.38E-03 | 4.52E-01
 | 2.5E-03 | 4.36E-02
Table of Validation Loss on Acceleration Mode
Name | Loss of X | Loss of V
Linear | 1.69E-03 | 4.70E-01
Naïve | 3.11E-03 | 5.25E-01
 | 1.95E-03 | 4.74E-01
 | 1.62E-03 | 4.05E-01
Name | Loss of X | Loss of V
Linear | 1.69E-03 | 4.70E-01
Naïve | 3.11E-03 | 5.25E-01
 | 1.95E-03 | 4.74E-01
 | 1.62E-03 | 4.05E-01
Table of Validation Loss on Deceleration Mode

## Slide 25: Preliminary Result of Acceleration Mode
Linear
Naive
Task: Given a series of inputs, predict the states of the system

## Slide 26: Preliminary Result of Deacceleration Mode
Linear
Naive
Task: Given a series of inputs, predict the states of the system

## Slide 27: QCar Digital Twin in Carla
“Carla is an Open-source simulator for autonomous driving research.”
Very active community in both academic and industry
Broad ecosystem: Carsim, NVIDIA SimReady
High fidelity image compared to its counterparts
Good Expandability and friendly APIs

## Slide 28: QCar Digital Twin in Carla
User Application
Carla Platform
Unreal Engine
Unreal Engine:
Image Rendering
Physics Simulation
Assets Management
……
Carla:
Wrapped Actor
Traffic & Pedestrian
Map Management
Additional Runtime Environment
User Application:
Retrieve Data
Apply Control
Set Policy & State
Reference: CARLA design - CARLA Simulator
Carla Architecture

## Slide 29: QCar Digital Twin in Carla
To easy the problem setting, we setup our physical model in Carla by disable the internal physics engine and set the physical state by ourselves.
It should be notes that this brings new issues, but most of them could be solved in the future version.
Break the API
Slower simulation
No collision

## Slide 30: QCar Digital Twin in Carla
2.b Physical State Update
2.a Sensor Collecting
3. World Tick
1. Carla Loop
Digital Twin Component
Proposed Framework

## Slide 31: QCar Digital Twin in Carla
Demo Video

## Slide 32: Thanks for listening